## Slide 1: 🤖 ROBOTICS COURSE — SESSION 8
Welcome to Robotics!
Let’s make the robot intelligent with a better performance

## Slide 2
🎯 TODAY’S GOAL
Today students will learn how to make Cutebot smarter
👁️ Use a filter to make better decisions from noisy sensor readings
📐 Apply PD control to adjust how strongly the robot turns
🔍 Create a recovery strategy so the robot can find the line again if it gets lost

## Slide 3
👁 The Robot Has 2 Eyes (Sensors)
L
R
L
R
← Left
Left on line
Turn LEFT
L
R
Right →
Right on line
Turn RIGHT
L
R
↑ Straight
Both on line
Go STRAIGHT
L
R
?? Search
No line seen!
SEARCH mode

## Slide 4
Code Overview
① Filter
45 sensor samples
Reads the sensor 45 times per cycle and counts votes. Removes noise so a single false reading doesn't steer the robot.
② PD Control
Proportional + Derivative
Computes a normalized error and applies kp (strength) and kd (damping) to smoothly correct direction without oscillating.
③ Search Mode
lastError memory
When the line is lost (whiteCount ≥ 30), the robot spins in the direction it last saw the line until it finds it again.

## Slide 5
🗳 The Filter — Let's Vote! (45 times)
The sensor is read 45 times. Each reading is a VOTE → the majority wins!
Robot drifts LEFT
← Left votes: 32 (32/45)
Right votes: 4 (4/45)
Center: 9 (9/45)
Turn RIGHT →
Robot is CENTERED
← Left: 5 (5/45)
Right: 6 → (6/45)
Center: 34 (34/45)
Go STRAIGHT ↑
Robot drifts RIGHT
← Left: 4 (4/45)
Right: 33 → (33/45)
Center: 8 (8/45)
Turn LEFT ←

## Slide 6
📐 PD Control — How Hard Should It Turn?
kp = 55 (Strength)
Small drift
→
Gentle turn
Medium drift
→
Medium turn
Big drift
→
Sharp turn
More drift = More correction!
kd = 20 (Brakes)
Without kd:
😵 Oscillates
With kd:
😊 Smooth curve!
kd brakes before overshoot!

## Slide 7
🔍 Search Mode — Find the Line Again!
1 On the Line
L
R
Robot follows the line.
lastError remembers
which side it drifted.
→
2 Line Lost! 😱
L
R
30+ white readings.
whiteCount ≥ 30
→ SEARCH MODE!
→
3 Searching...
L
R
Spin the way lastError
points. Keep spinning
until line found!
🧠 lastError = memory! Robot always knows which way to turn.

## Slide 8
👁
① Sample
Read sensor
45 times
→
🗳
② Filter
Count votes
Find majority
→
📐
③ Control
kp × error
+ kd × change
→
🚗
④ Move!
Set wheel
speeds
⚙️ Parameters:
baseStraight = 45
baseTurn = 30
kp = 55
kd = 20
searchSpeed = 45
samples = 45
threshold =
30 / ±5
🔍 If whiteCount ≥ 30 → Skip control → Spin toward lastError direction until line is found again!

## Slide 9
👨‍💻 ROBOT CODE

## Slide 10
let lastError = 0
let dError = 0
let normError = 0
let whiteCount = 0
let sumError = 0
let baseStraight = 40
let baseTurn = 30
let kp = 20
let kd = 8
let searchSpeed = 45
basic.showIcon(IconNames.Square)
basic.forever(function () {
  sumError = 0
  whiteCount = 0
  for (let index = 0; index < 45; index++) {
    // intersección
    if (cuteBot.tracking(cuteBot.TrackingState.L_line_R_unline)) {
    sumError += -1
    } else if (cuteBot.tracking(cuteBot.TrackingState.L_unline_R_line)) {
    sumError += 1
    } else if (cuteBot.tracking(cuteBot.TrackingState.L_R_line)) {
    } else {
    whiteCount += 1
    }
  }
  normError = sumError / 45
  dError = normError - lastError
  if (whiteCount >= 30) {
  cuteBot.motors(lastError * searchSpeed, (0 - lastError) * searchSpeed)
  } else {
    if (sumError <= -5) {
    lastError = -1
    } else if (sumError >= 5) {
    lastError = 1
    }
    cuteBot.motors(baseStraight + kp * normError + kd * dError, baseStraight - kp * normError - kd * dError)
  }
})